## Slide 1: General and Chemical Laboratory Safety Training
For Laboratory Teaching Assistants and Research Students
Presented by Heath de la Giroday,
Dispensing Chemist, Chemical Safety Officer, Radiation Safety Officer

## Slide 2: Why Safety Training?
Career development
To prevent injury and maintain your lifestyle
The University has a legal and ethical obligation to protect each student, assistant, faculty, and staff member

## Slide 3: Who is in Charge of Safety
Everyone on campus is part of our safety apparatus
  You
    Participate in training, comprehend information, report safety issues, ask questions, follow procedures
  Supervisor/manager/SLI
    Providing specific/specialized training, provide PPE, monitor activities, develop and maintain safe work plans
  Dispensing Chemist (Chemical and Radiation Safety Officer)
    Assist in achieving regulatory compliance, develop proactive strategies, provide training, monitor safety of laboratories

## Slide 4: Who is in Charge of Safety
Risk & Safety Coordinator
  Assist in achieving regulatory compliance, develop proactive strategies, provide training, monitor safety of laboratories
Laboratory Safety Committee
  Develop policy and procedures, provide guidance for development of lab safety structure, make recommendation to JOHS Committee
Joint Occupational Health & Safety Committee

## Slide 5: Introduction to the Laboratory

## Slide 6: Let’s Get Started!
Safety resources and locations
Hazards
Laboratory Hygiene and Habits
MSDS
Personal Protective Equipment
Fumehoods and BSCs
Signs and Labeling
Spills and Accidents
Waste/Disposal
Gases

## Slide 7: Information Resources
Chemical Safety and Methodology Manual
  Provides laboratory and chemical safety procedures
  Provides waste disposal information
Biosafety Manual
Chemstores Website
Coming in the new year—Laboratory Safety Website

## Slide 8: Safety Resources and Locations
  Know your exit doors
  Know where the fire alarm is in proximity to your laboratory
  Be aware of the fire extinguishers, fire blankets in location near your laboratory
  Know where the eye wash/safety shower is located
    Is it unobstructed?
  Know location of spill kit
    Go through contents of spill kit each semester if you are a supervisor/TA

## Slide 9: Know Your Surroundings
Each laboratory has a telephone in a designated area for use
The emergency contact numbers are posted near the phone in every laboratory on the UNBC campus
Test this phone to ensure it is working

## Slide 10: Know What Hazards are Present

## Slide 11: Hazards
Many laboratories contain hazardous substances.
  A hazardous substance is defined as a material/substance that poses a physical or health hazard. This includes both chemical and biological agents
There are differences between a health hazard and a physical hazard

## Slide 12: Health Hazards
A health hazard has the following characteristics:
  Carcinogen
  Toxic or highly toxic
  Reproductive Toxins
  Irritants
  Corrosives
  Sensitizers
  Hepatotoxins
  Nephrotoxins
  Neurotoxins

## Slide 13: Physical Hazards
A physical hazard has one or more of the following characteristics:
  Explosive
  Corrosive
  Flammable
  Oxidizer
  Pyrophoric
  Organic peroxide
  Compressed gas
  Unstable (Reactive)
  Water-reactive

## Slide 14: Laboratory Hygiene

## Slide 15: Chemical Hygiene Plan
When a chemical is in the laboratory, the hazards of that chemical must be communicated to you
A Chemical Hygiene Plan (CHP) relays information regarding procedures, equipment, PPE, and work practices that are capable of protecting students/employees from health hazards

## Slide 16: Chemical Hygiene Plan
The CHP also prevents contamination and exposure
  Placing lab coats on hooks in lab
  Sending lab coats for cleaning on a regular basis
  Labeling computers for glove or no glove use
  Dedicating a bench for toxic or mutagenic substances
Supervisors (TAs, PIs, SLIs) are responsible for communicating this information

## Slide 17: Lab Attire
You should remember the following:
  Shoes must completely cover feet
  No shorts—legs must be covered
    Consider keeping a change of clothes available
  Restrain hair when working with hazardous materials
  Remove protective clothing and gloves in public to avoid contamination of public spaces
  Apparel should match what is happening in the lab, not what you are doing

## Slide 18: Personal Habits
Personal habits play a large role in minimizing hazards. The following measures must be taken:
  Do not eat, drink, smoke, chew gum or apply cosmetics, or remove/insert contact lenses while in the laboratory
  Do not store food or beverages in the lab or in chemical refrigerator
  Do not mouth pipette
  Wash hands before leaving laboratory or after handling contaminated material

## Slide 19: Safe Practices
Safe practices to ensure safe working conditions:
  Do not use chipped or cracked glassware
  When working with hazardous materials, have a second person nearby
  Know emergency procedures
  Keep the laboratory neat and clean
  Use hazardous chemicals under a fume hood and biohazardous materials under a biological safety cabinet (BSC)
  Decontaminate as needed
  All procedures should be performed to minimize aerosol generation

## Slide 20: Laboratory Emergency Plan

## Slide 21: Laboratory Information
Each lab contains an Emergency Action Plan which is required for emergency situations
This is used to inform faculty/staff/students of the procedures to follow in the event of an emergency

## Slide 22: WHMIS

## Slide 23: WHMIS
Workplace Hazardous Material Information System
Classifications
  A. Compressed gas
  B. Flammable and combustible
  C. Oxidizer
  D. Poisonous/infectious
    D1 Immediate toxic effects
    D2 Other toxic effects
    D3 Infectious
  E. Corrosive
  F. Dangerously reactive material

## Slide 24: Labeling
It is important to know as much about a chemical as possible.
The most dangerous substance is the one that has no label.

## Slide 25: Labelling
One must remember that if any chemical is transferred to a secondary container, this container must be labeled with the chemical name and concentration
If the chemical will be used by the end of the work shift, then labeling is not necessary
  If it is not consumed by the end of the shift, you have an obligation and responsibility to label it
  Max of 3 hours
  Cannot be out of personal presence
Good science practices would encourage you to label all containers

## Slide 26: WHMIS in the Lab
Laboratory exemption for less than 10kg container
Laboratory Labels
  A. Laboratory Supply House Container
    Product identifier
    Reference to MSDS
    Risk phrases
    Precautionary measures
    First aid measures
  B. Laboratory Container
    Product identifier (name)
    Cannot leave laboratory (the room)—if it will be moved between rooms, it needs full labeling (available from Chemstores for free)
  C. Samples for Analysis
    Product identifier (name)
    Cannot leave laboratory or will require further labeling

## Slide 27: Labeling Tips
Make it legible
Make it universal
  e.g., “Iron Reagent” does not provide sufficient information for clean up or disposal
Re-write labels that are fading as soon as you notice it
Water containers must be labeled
  Clear liquids are not water by default

## Slide 28: GHS
Over the next three years WHMIS is receiving an overhaul through GHS
  Additional symbols
  New classes of hazards
  Global harmonization
Additional training will be provided

## Slide 29: WHMIS
Employee “right-to-know” legislation
  Education regarding WHMIS system
  Education regarding hazards of specific chemicals that are used under normal conditions
  Chemicals must be labelled
  MSDS must be readily available
Three parts
  System education
  Implementation
  Role-specific training

## Slide 30: MSDS

## Slide 31: Material Safety Data Sheets (MSDS)
In addition to labeling in a laboratory, the next most important type of communication regarding hazards is the MSDS.
This will communicate the information necessary regarding various hazards associated with chemicals and biological agents.

## Slide 32: Reading the MSDS
MSDS are broken down into sections
Canadian WHIMS dictates 9 sections
International standard is 16
Comparison of MSDS headings in WHMIS legislation and other standards (ANSI, GHS) |  |  | 
WHMIS (Canadian) |  | ANSI / GHS | 
Item | Heading suggested in CPR schedule | Section | Heading
1 | Hazardous Ingredients | 1 | Product and Company Identification
2 | Preparation Information | 2 | Hazards Identification
3 | Product Information | 3 | Composition/Information on Ingredients
4 | Physical Data | 4 | First Aid Measures
5 | Fire or Explosion Hazard | 5 | Fire Fighting Measures
6 | Reactivity Data | 6 | Accidental Release Measures
7 | Toxicological Properties | 7 | Handling and Storage
8 | Preventive Measures | 8 | Exposure Controls/Personal Protection
9 | First Aid Measures | 9 | Physical and Chemical Properties
 |  | 10 | Stability and Reactivity
 |  | 11 | Toxicological Information
 |  | 12 | Ecological Information
 |  | 13 | Disposal Considerations
 |  | 14 | Transport Information
 |  | 15 | Regulatory Information
 |  | 16 | Other Information

## Slide 33: Laboratory Information
Why is an MSDS important? When you know characteristics about a substance it can aid in precautionary measure to take when using it
Also, if there is a spill either on a surface or on your skin, the MSDS can supply you with the response measures

## Slide 34: MSDS
The MSDS to every chemical in your lab must be available to you
It may be in a notebook or available over the internet
Make sure you find the location of the MSDSs in your room

## Slide 35: MSDS Recommendation
Read the relevant portions of the MSDS for every chemical you use at least once
  e.g., PPE, handling precautions, physical properties (flash point)
  This is a small investment that can protect you
There may be protection, storage, or first aid requirements that you or your supervisor are unaware of
  Methanol-can absorb through skin
  Can cause liver and kidney disorders

## Slide 36: MSDS at UNBC
There is a link from the Chemstores website to searchable MSDS database maintained by the Canadian Centre for Occupational Health and Safety

## Slide 37: Sample MSDS

## Slide 38: Chemical Inventory

## Slide 39: Inventory
Fire response plan
  Used by fire department during pre-incident planning and during incident response
WorkSafeBC requirement
  Inventory and MSDS must available
Fire Code
  Maximum volumes allowed in a room (1500L)
Encourages use of materials already on campus

## Slide 40: UNBC Chemical Inventory
Barcodes are placed on chemicals when they arrive
The chemical is entered into the Vertere chemical inventory
Vertere is used to generate all
documents

## Slide 42: Vertere Inventory
Consumed chemicals
  Email the number to the Dispensing Chemist
  Deface the barcode
Physical inventory is performed
every year

## Slide 43: Personal Protective Equipment

## Slide 44: PPE
Acronym for personal protective equipment
This is the equipment that is necessary to protect yourself from hazardous materials

## Slide 45: Chemicals & PPE
When chemicals are being used there is always the possibility of a spill
The proper PPE to use when chemicals are involved would include:
  Eye/face protection: safety glasses, goggles, face shield
  Hand protection (Gloves): nitrile, rubber, latex, PVC
  Body: lab jacket, apron
  Lungs: respirator, fume hood

## Slide 46: Protection Is Variable
Gloves are variably permeable to chemicals
  Duration of contact, chemical, concentration, pH, carrier solvents, potential for cuts, abrasiveness, and quantity
Safety glasses, goggles, faceshield
  Chemical, quantity, height, pressurized system, and environment
Respirator
  Chemical, particulate/aerosol size, exposure duration, and environment

## Slide 47: Protection Is Variable
More information is often needed to select PPE
  Glove selection table, TWA

## Slide 48: Use of PPE
Knowing how to properly use PPE can be the key to adequate protection.
Not only do you want to make sure it is the proper size for you, but also make sure you are wearing it properly.
  e.g., fit tests are required for respirators
Let your supervisor know if you need a different size.
  PPE is relatively cheap compared to other items in a lab or the cost of an injury
  Poorly sized PPE does not get used as often

## Slide 49: Fume Hoods and BSCs

## Slide 50: Engineering Controls
Let’s look at the following barriers:
Fume hood
Biological Safety Cabinet (BSC)

## Slide 51: Fume Hood
The fume hood is used with chemicals
The main function is to exhaust the vapors, aerosols, and gases to the atmosphere
The hood is designed to minimize your exposure to airborne contaminants
  This is not to be used with biohazardous materials due to insufficient filtration/treatment

## Slide 52: Fume Hood Use
Ensure the exhaust blower is operating and air is entering the hood
Remember, do not put your face inside the hood!
Minimize storage of chemicals or other items in the hood
Clean spills immediately
Work with the sash at the proper operating level as indicated by the arrows
  Check it everyday

## Slide 53: Things to Think About
Avoid obstructing airflow
Avoid placing lightweight items in the hood that can be drawn into the exhaust system
  Paper towels
  Pieces of styrofoam
Fumehoods do not function during power outages
  Work cannot continue

## Slide 54: Fume Hoods
When not in use, containers should be capped
Fume hoods should be turned off when not in use, unless this poses a clear hazard
  Fume hoods are massive energy consumers
    They vent heated/filtered/cooled air directly to the environment
  Close hood, flick switch, and hit alarm silence button
  If additional hazard is created (e.g., heavy winds move air through ducts) leave it on

## Slide 55: Biological Safety Cabinet
The biological safety cabinet (BSC) is used as a containment for infectious agents
  Uses HEPA filter to filter exhausted air
high efficiency particulate air filter is able to remove particles at a size of 0.3 um with a minimum efficiency of 99.97%
There are several designs of BSC
  Filter and recirculate air
  Filter and exhaust air

## Slide 56: Signs

## Slide 57: NFPA Hazard Signs
NFPA hazard signs are located on every lab door
Guides first responders
Highly recommended that a protective equipment worn at all times for rating 2 and up

## Slide 58: Spills and Accidents

## Slide 59: Most Major Accidents Are Preceded by Close Calls
Remember that most major accidents are highly predictable
  Close calls
  Smaller incidents

## Slide 60: Spill Classification
No-hazard
  Does not represent a substantial hazard if cleaned immediately
  Can be cleaned with common cleaning materials
Low-hazard (Low-hazard Spill Form must be submitted)
  Requires contents of spill kit
  Requires support from janitorial to clean
Hazardous (Must be reported to Safety Officer)
  Represents serious hazard to personnel, environment, or facility due to location, chemical properties, quantity, or situation
  Requires additional personnel or equipment for clean up
  Eye wash or safety shower used or contaminated

## Slide 61: SOP
Spills and accidents can pose a serious health and safety threat
Standard Operating Procedures should be available for spills
General Example
  Identify all hazards
  Inform others
  Refer to the MSDS
  Collect PPE
  Clean spill
  Decontaminate area

## Slide 62: Aerosols
When a spill occurs, an aerosol can be created which can make the material several times more potent as a inhalation hazard
Allow sufficient time for the aerosol to settle before entering the room

## Slide 63: Spill Kits
There is a spill kit in your lab, find its location
Basic Spill Kit
  Absorbants/neutralizers
  Bag
  Marker
  Gloves
  Scraper or broom
  Eye protection

## Slide 64: Clean Up Tips
Always clean work from the outside inwards to avoid spreading contamination
    Add neutralizing absorbents slowly—neutralization reactions can be extremely exothermic
Move contaminated items onto a disposable bench cover, clean the surface, then clean the items and place them back on the surface

## Slide 65: Emergency Situation
Focus on mitigating damage:
  People are number one priority
  Environment
  Equipment
Contact Security
Refer to MSDS sheets (they should be easily accessible)
  They will inform your response

## Slide 66: How to Report
When a hazardous spill occurs, it must be reported to your supervisor
If a spill kit is accessed, a low-hazard spill report form must be filled out
All injuries that are a result of a spill must be reported to Dispensing Chemist (250-960-6472) and Risk & Safety Coordinator (250-960-5530)

## Slide 67: Waste Management

## Slide 68: Waste
Hazardous and biohazardous wastes have special guidelines for proper disposal
It is important to properly dispose of waste to ensure human and environmental health
Necessary for regulatory compliance

## Slide 69: Non-hazardous Waste
Normal disposal, unless it will cause undue concern
  e.g., looks dangerous or disconcerting

## Slide 70: UNBC Waste Streams

## Slide 71: Waste
Hazardous Waste- This is a waste which contains the characteristics of being any of the following:
  Toxic (human or environment)
  Corrosive
  Ignitable
  Flammable
  Oxidizer

## Slide 72: Hazardous Waste
Neutralized to non-hazardous waste, when possible
Disposed of through Clean Harbors
  Incineration, stabilization, land fill, recycling
Stored in secure, well-ventilated areas

## Slide 73: Liquid Waste
UNBC has 4 liquid hazardous chemical waste streams
  Toxic aqueous
  Organic
  Organic halogenated
  Oxidizer

## Slide 74: Liquid Waste
Important to check for compatibility before adding
  Some wastes will react
  Check MSDS for incompatibilities
Extremely toxic wastes should be kept separate
It is possible to contaminate waste
  e.g., add 1 drop of methyl mercury to 4 L of acetone/hexanes extraction waste. Now it is 4 L of mercury waste

## Slide 75: Liquid Waste
Guidelines
  Wastes must be compatible (should not be reacting)
  Waste bottles must be tagged
    Waste type
    Date started
    Date Finished
    All contents indicated with volume added or % by volume of the container
    Laboratory (PI, SLI, room)
  Should not be overfilled
  Waste bottles must be replaced every year

## Slide 76: Waste
Note: Hazardous Waste disposal can be extremely expensive and hazardous
  Unlabeled containers
  Highly reactive substances (organic peroxides)
  Incorrectly labeled containers
  Complex solutions
  Old containers
    Some reactions occur slowly, making old containers less predictable

## Slide 77: Solid Waste and Contaminated Items
Place in a sealed plastic bag, bucket, or glass container
  Label with chemical content
  Lab name/number
  Date

## Slide 78: Biohazardous Waste
A biohazardous waste is any waste that is considered infectious and/or because of its biological nature it can cause physical or health hazards in humans, animals, plants or the environment.
This includes recombinant DNA and other genetically altered organisms and agents.
Biological waste is not necessarily biohazardous.

## Slide 79: Biological Waste
Non-putrefying, undiseased/poisonous animal/plant tissues
  Less than 5lbs
    Drain excess liquid, place in a sealed plastic bag
    Mark name and date
    Place in a cardboard box labeled waste
    Dispose via normal garbage
  Less than 20lbs
    Same, except dispose into compactor

## Slide 80: Biohazardous Waste
Waste that is considered potentially biohazardous can be disposed of in regular trash if it has been rendered non-infectious/non-hazardous
  e.g., Autoclave or bleach, if applicable
Biohazardous waste is disposed of in the biomedical waste buckets
  Red—Tissue, samples (shipped to Delta for incineration)
  Yellow—Materials contaminated with biohazardous waste (shipped to delta for commercial autoclaving)

## Slide 81: Hazardous Wastes
All hazardous wastes must be brought to the Dispensing Chemist

## Slide 82: What is a Sharp?

## Slide 83: What is a “Sharp”?
A sharp is defined as any instrument, tool, or item that has rigid, acute edges, protuberances or corners capable of cutting, piercing, ripping or puncturing
  e.g., syringes, blades, jagged metal, and broken glass
Items that have the potential for becoming sharps are considered sharps
http://www.ehrs.upenn.edu/training/bloodborne/bloodborne.html

## Slide 84: Safe Practices
When using a sharp there is a risk of being cut by the object and possible poisoning/infection occurring
  Sharps injuries are very serious
    Unkowns associated with injuries (contaminated wounds)
    UNBC personnel have been injured by careless disposal
    Treatments associated with “sticks” are expensive, intensive, and unpleasant
Special precautions are used for hypodermic needles to avoid a needlestick
  Do not recap, place directly in the sharps container

## Slide 85: Disposal of Sharps
All sharps must be placed into a rigid, puncture and leak-resistant container that is also impervious to moisture
The sharps container must be labeled either with “Biohazard” or “Infectious Waste”
  If there is additional contamination, a separate container may be necessary
Do not put other items in or overfill sharps containers

## Slide 86: Disposal of Sharps Containers
When the sharps container is full it must be taken to Chemstores
If there is a large amount, the Dispensing Chemist (250-960-6472) will come and pick it up
There must be a chain of custody with all waste

## Slide 87: Gases

## Slide 88: Gases
Gases are physical and health hazards
  Compressed gas containers can become powerful, dangerous projectiles if the vessel is compromised
The vented gas may be an asphyxiant, oxidizer, flammable, corrosive, or toxin
  Oxidizer and flammable may be an explosive combination

## Slide 89: Atmospheric Displacement Asphyxiation
Venting of compressed gas or evaporation of cryogenic liquids displaces atmospheric
Oxygen deficient atmosphere can result in rapid loss of consciousness (1-2 breaths or 5-9 seconds)
Notes: Respiration of oxygen deficient gases results in loss of internal oxygen reserves as oxygen diffuses out of the blood along the concentration gradient.

## Slide 90: Compressed Gases
  They should be stored with a secure, approved strap or chain
  Always keep covers on compressed gas cylinders when not in use
  To move gas cylinders secure the cylinder in the tank dolly using the strap and make sure the cap is fastened

## Slide 91: Regulators on Gas Cylinders
Connecting a pressurized cylinder to a closed system can overpressurize the closed system resulting in injury or equipment damage
Always make sure the regulator is completely closed before opening the tank valve and then slowly open the regulator to a safe pressure
Know the safe operating pressure of the system you are using

## Slide 92: Cryogenic Liquids
Hazards
  Asphyxiation
  Freezing damage
  Overpressure bursting of vessels
  Generating liquid oxygen (oxidizer)
Liquid | Expansion Ratio (from BP to 21C) | Boiling Point
Nitrogen | 696 | -195.8ºC
Argon | 841 | -185.9ºC
Helium | 754 | -268.9ºC
Neon | 1445 | -246.1ºC
Oxygen | 860.5 | -183 ºC

## Slide 93: Cryogenic Liquids
Small spaces with poor air exchange are dangerous
  Do not allow others to ride in elevator while transporting (use buddy system if possible)
  Do not transport inside vehicle passenger compartment
  Ensure that substantial air exchange occurs before going near a spill
Evacuate people away from spills
Wear appropriate PPE (pants, closed shoes, face shield, insulated gloves)

## Slide 94: Accountability/Discipline
Supervisor is responsible for your conduct in the lab
The CSO, BSO, and RSC will talk to you if you are doing something unsafe
You will be asked to leave the laboratory if you are in breach of UNBC policies/procedures
  Your supervisor will be contacted
  If there are repeated offences, the issue will be brought to the Lab Safety Committee and the Dean of the College